Recommended Improvements to Kinematic Methods: Current implementations of incremental moves should be improved.

Consider a pure motion of spin of the hand's grasp frame about a chosen spin axis—e.g., the palm normal. The normalizedd 6x1 Cartesian-space twist vector corresponding to this task-space motion (and expressed in hand grasp-frame coordinates) would be: t_spin = [0,0,0,0,0,1]T. A joint-space velocity vector, qdelta_spin, that produces this target twist can be solved from the relation: t_spin = J qdelta_spin. If a solution to this equation is qdelta_spin, then any scaled value of this joint-space velocity vector may be added to the nominal solution. Equivalently, this vector of joint-angle displacements may be appended to the null-space matrix, N, so this degree of freedom may be considered simultaneously with all other null-space vectors. This will increase the dimension of the null-space weight vector, n_null. This increased dimension opens up more options for producing an acceptable hand-motion solution while optimizing other factors, including joint velocity limits and joint range limits.

1) given 6DOF target pose (e.g. for grabIt)
try first to match desired orientation and height (and consider joint limits and collisions);
        if can reach the above “approach” pose safely, do so.
        Conclude the move with pure motion along approach (palm-normal) axis while preserving orientation.

To do this, assume n degrees of freedom of robot (n joints involved, e.g. 7).

from approach pose, have desired twist vector of [0,0,vz,0,0,0] = twist_des_transpose

move as qdot = J_pinv*twist_des
  (if freeze torso and pelvis, this is unique)

fix drift: plan is to go from pose_init to pose_goal
at each step, have expected pose (R_goal; [x_goal, y_goal, z_goal-d*z_dir] in grasp frame)

get current pose based on commanded angles: x(q_cmd), y(q_cmd), z(q_cmd), R(q_cmd)

Compute drift errors: x_err = x_goal-x(q_cmd), y_err=, z_err=...
R_err = R_goal – R(q_cmd)

create twist-correction vector: t_correction = eps*[x_err, y_err, z_err, dphi_x_err, dphi_y_err, dphi_z_err];

(eps has units of 1/time, so result is a twist velocity vector; this might be, e.g., a correction to take place over a few time steps)

compute dq_correction = J_pinv*t_correction

add dq_correction to qdot and execute it.

2) 5-dof target w/ spin-axis freedom
  assumes have specified spin axis, e.g. palm normal (for palming an object, such as valve)
  call this [x_goal, y_goal, z_goal] and b_des

  align b_des, using twist_des = eps*[x_err, y_err, 0, phi_err_vec],
    where phi_err_vec = b_des.cross(b_hand), and eps is units 1/time
    exert corresponding qdot = J_pinv*twist_des to converge on pose error:
      [0,0,z_err], b_des = b_hand

    execute approach along b_hand, correcting for drift, but allowing rotation about b_des.

    Above qdot is OK, but have options of N = [ker(J_6xn)|qdot_spin]
   where qdot_spin = J_pinv*[0,0,0,0,0,1]'
    (joint motion resulting in pure rotation about b_hand is allowed as a null-space vector)

3) SPECIAL CASES: y-axis vertical: try approach pose to use torso joint (w/ approach pose computed correspondingly)
        z-axis vertical: try approac pose to use squat motion

4) prioritized approach (e.g., permit some angular error)