Electro-hydraulic actuator dynamic modeling:

Assume an actuator has a left side with pressure P_l and volume V_l, and fluid mass m_l, and a right side with P_r, V_r, m_r. A piston of area A separates the halves, and the resultant actuator effort is: e= A*(P_r-P_l).

The left side is exposed to a pressure source either P_high or P_low through an orifice with conductance G_left(i). The pressure source on the left side can be expressed as:

P_sl = (P_high+P_low)/2 + sgn(i)*(P_high-P_low)/2 = P_mean + sgn(i)*P_delta

That is, the source pressure on the left side is P_high for i>0 and P_low for i<0.

On the right side, an orifice from the right chamber is exposed to pressure:

P_sr = P_mean – sgn(i)*P_delta

The flow conductance, |G(i)|, is a non-negative function that increases with the magnitude of the control current, i.

From PV=mRT, we have that:
P_l*V_l= m_l*(RT)
P_r*V_r = m_r*(RT)

Differentiating,
Pdot_l*V_l + P_l*Vdot_l = mdot_l*(RT)
Pdot_r*V_r + P_r*Vdot_r = -mdot_r*(RT)
Note that in the second equation, mass flow is defined as positive out of the right volume.

if the piston moves with velocity “v”, then:
Vdot_l = A*v
Vdot_r = -A*v

Fluid flows through the left and right orifices, constrained by the pressure drop and the flow conductance. Assume that the flow conductances |G_l(i)|=|G_r(i)|, since ports are exposed by the same amount via a common control spool.

The fluid flow rates, mdot_r and mdot_l, follow from:
mdot_l = |G(i)|*(P_sl – P_l)
and
mdot_r = |G(i)|*(P_sr – P_r)

Substituting for P_sl and P_sr,
mdot_l = |G(i)|*(P_mean + sgn(i)*P_delta– P_l), and
mdot_r = G(i)|*(P_mean – sgn(i)*P_delta– P_r)

Using the above expressions for mdot in the pressure equations results in:
Pdot_l*V_l + P_l*Vdot_l = (RT)*|G(i)|*(P_mean + sgn(i)*P_delta– P_l)
Pdot_r*V_r + P_r*Vdot_r = -(RT)*G(i)|*(P_mean – sgn(i)*P_delta– P_r)

Substituting for Vdot, and rearranging, it follows that:

Pdot_l*V_l = - P_l*A*v+ (RT)*|G(i)|*(P_mean + sgn(i)*P_delta– P_l)
Pdot_r*V_r = P_r*A*v -(RT)*G(i)|*(P_mean – sgn(i)*P_delta– P_r)

If the left and right volumes are approximatly equal (e.g., actuator centered and making smal motions), then we can approximate V_l = V_r = V, and thus:

Pdot_l= - P_l*A*v/V + (RT)*|G(i)|*(P_mean + sgn(i)*P_delta– P_l)/V
Pdot_r= P_r*A*v/V -(RT)*|G(i)|*(P_mean – sgn(i)*P_delta– P_r)/V

Subtracting these equations, we get:
Pdot_l – Pdot_r = -(P_l+P_r)*(A/V)*v + (RT/V)*|G(i)|*[2*P_delta*sgn(i)-P_l+P_r]

But e = A*(P_l-P_r), and thus:

e_dot = -(A*A/V)*(P_l+P_r)*v +(RT/V)*|G(i)|*[e_max -e]

where e_max = A*(P_high – P_low)

If we can approximate that P_l+P_r is nearly constant, then:

e_dot = -K_ve*v + f_G(i)*[e_max – e]

For constant velocity conditions (or slowly varying velocity), i.e. quasi steady-state, e_dot=0, and thus:

v = f_G(i)/K_ve*[e_max – e]

Typically, e = e_Coulomb for constant velocity. Roughly (for the forearm), v = 3*i_cmd, from which we get:
f_G(i)*[e_max-e_Coulomb]/K_ve = 3*i

Also, for high-speed tests, with rapidly-varying i(t) and v(t) nearly constant, expect:
e_dot = f_G(i)*[e_max-e]
  and thus f_G(i) = 1/tau, defining the time constant tau via the slope of the pressure response.