Multi-segment Path Specifications
Wyatt Newman
February, 2015

ROS has extensive support for navigation, known as the “nav stack” (see: http://wiki.ros.org/navigation). A planned path is conventionally communicated as a message of type nav_msgs/Path.msg, which contains a vector of (stamped) poses. These poses are of type geometry_msgs/Pose, which is in turn comprised of a point and a quaternion. In short, a ROS path is equivalent to an ordered list of frames. This path specification is not suitable for immediate execution; it requires some refinement for achieving a desirable trajectory.

A corresponding simple path description may be specified as a polyline: a sequence of line segments connected at listed vertices (origins of successive frames). In such a description, vertices of the polyline correspond to discontinuities of heading. Since a real robot has inertia, instantaneous change in heading is impossible. If the robot attempted to maintain constant speed through a vertex, it would require an instantaneous change in momentum, which would require infinite force and torque.

To follow a polyline precisely, the robot must start each line segment from rest, then come to a full stop at each vertex. At a vertex, the robot must spin in place, ramping the angular velocity up from zero and back down to zero. After a spin-in-place—which results in the robot aligned with the next line segment—the robot can begin to ramp up its translational velocity to travel along this line segment. In some instances, this can be a reasonable strategy. With reference to the 2nd floor of Glennan, starting in front of the elevator and pointing towards the lab door, the first path segment may proceed forward, come to a full halt approximately 2m in front of the lab door, spin in place by -90 deg, then proceed down the long hall.

A faster trajectory would avoid coming to a complete halt. Instead, a line segment may blend into a circular arc, and hence to another line segment. This would allow continuous motion by rounding the corners of a polyline.

Although more general path segments can be considered, adequate paths can be constructed with just these three segment types: line segments, circular arcs and spin-in-place rotations.

*convert pose list to lines/arcs
-e.g., assume fixed arc radius;
  - consider only origins of successive poses to define polyline (except last pose)
  - for successive line segments, consider blending arc of radius “r”
  - if pts are too close together, coerce spin-in-place segments, else insert arc
  - (must have arc or spin between each lineseg)
  - generate path with limited look-ahead, converting to odom frame
  - (don't convert all in advance, else odom will drift too far)
*desired-state generation from cwru path-list:
  - vel scheduler: a and alpha; v_max, omega_max;
  - v_des and omega_des;
  - desired pose(t): x,y, heading (tangent), curvature
  - stop state_des generation if halt condition (e-stop, LIDAR, software halt)

PathSegment.msg
#Reference frame that the following coordinates should be interpreted relative to and timestamp to use when transforming
Header header

#Segment type enums
int8 LINE = 1
int8 ARC = 2
int8 SPIN_IN_PLACE = 3

#Segment type
int8 seg_type

#Segment number
uint32 seg_number

#Segment length
float64 seg_length

#Reference point
geometry_msgs/Point ref_point

#Initial tanget angle
geometry_msgs/Quaternion init_tan_angle

#Curvature
float64 curvature

#Speed limits for this segment
geometry_msgs/Twist max_speeds
geometry_msgs/Twist min_speeds

#Acceleration limit for this segment (m/s^2 for lines/arcs, rads/s^2 for spin-in-place)
float64 accel_limit

#Deceleration limit for this segment
float64 decel_limit

Desired state:
#Standard ROS header for timestamp and frame_id
Header header

#Segment type
int8 seg_type

#Segment number
uint32 seg_number

#6DOF pose
geometry_msgs/Pose des_pose

#Desired speed
float64 des_speed

#Desired curvature
float64 des_rho

#Desired distance along the segment
float64 des_lseg