Multi-segment Path Specifications
Wyatt Newman
February, 2015

A simple path description may be specified as a polyline: a sequence of connected line segments. In such a description, vertices of the polyline correspond to discontinuities of heading. Since a real robot has inertia, instantaneous change in heading is impossible. To follow such a path, the robot must start each line segment from rest, then come to a full stop at each vertex. At a vertex, the robot must spin in place, ramping the angular velocity up from and back down to zero. This initiates translational velocity ramping for the next line segment. This can be a reasonable strategy. With reference to the 2nd floor of Glennan, starting in front of the elevator and headed towards the lab door, the first path segment may proceed forward, come to a full halt approximately 2m in front of the lab door, spin in place by -90 deg, then proceed down the long hall.

A faster trajectory would avoid coming to a complete halt. Instead, a line segment may blend into a circular arc, and hence to another line segment. This would allow continuous motion by rounding the corner of the polyline.

Although more general path segments can be considered, adequate paths can be constructed with just these three segment types: line segments, circular arcs and spin-in-place rotations.

 e.g. making forward progress, coming to a full halt rotating -90 deg